## Slide 1: Gazebo
Ling Chen ( lcheno@shu.edu.cn )
From
Shanghai University

## Slide 2: Gazebo
Gazebo
  – is a multi-robot simulator
  – can simulate a population of robots, sensors and objects in a
  three-dimensional world.
  – includes an accurate simulation of rigid-body physics and
  generates realistic sensor feedback
  – allows code designed to operate a physical robot to be executed
  in an artificial environment

## Slide 3: Gazebo Features
Dynamics Simulation
  –Direct control over physics engine parameters
Building Editor
  –Construct a 3D model of a building within the Gazebo UI, without writing a line of code
Advanced 3D Graphics
  –State-of-the-art GPU shaders generate correct lighting and shadows for improved realism.
Sensors
  –Support for laser range finders, 2D cameras, Kinect style sensors, contact sensors, and RFID sensors

## Slide 4: Gazebo Features
• Robot Models
– Many robots are provided including PR2, iRobot
Create, TurtleBot, generic robot arms and grippers
• Environments
– Access to many objects from simple shapes to
terrain
• Programmatic Interfaces
– Support for ROS
– API for custom interfaces

## Slide 5: Gazebo Architecture
• Gazebo runs two processes:
• Server: Runs the physics loop and generates sensor data.
  – Executable: gzserver
– Libraries: Physics, Sensors, Rendering, Transport
• Client: Provides user interaction and visualization of a simulation.
  – Executable: gzclient
  – Libraries: Transport, Rendering, GUI

## Slide 6: Running Gazebo
Run Gazebo server and client separately:
Run Gazebo server and client simultaneously:
Run from ROS
$gzserver
$gzclient
$rosrun gazebo_ros gazebo
$gazebo

## Slide 7: Gazebo Run from ROS

## Slide 8: World Description File
• The world description file contains all the elements in a simulation, including robots, lights, sensors, and static objects.
• This file is formatted using SDF (Simulation Description format), and has a .world extension
• The Gazebo server (gzserver) reads this file to generate and populate a world.

## Slide 9: Try: Gazebo
A number of example worlds are available
– /usr/share/gazebo-2.2/worlds
roslaunch to open world models:
– open willowgarage_world:
Note: if model cannot be downloaded, copy to ~/.gazebo/
$roslaunch gazebo_ros willowgarage_world.launch

## Slide 10: Willow Garage World

## Slide 11: How to use Gazebo to simulate your robot
Steps:
1. load a world;
2. load the description of the robot;
3. spawn the robot in the world
4. publish joints states
5. publish robot states
6. run rviz
$roslaunch pioneer_gazebo pioneer_world.launch
$roslaunch pioneer_description pioneer_rviz.launch

## Slide 12: Gazebo: Robot Simulation

## Slide 13: Rviz: Robot Simulation

## Slide 14: 1.Load a world
See file="$(find gazebo_ros)/launch/empty_world.launch"

## Slide 15: 2. Load the description of the robot
Using xacro:
Xacro (XML Macros) Xacro is an XML macro language. With xacro, you can construct shorter and more readable XML files by using macros that expand to larger XML expressions.
More details: http://wiki.ros.org/xacro
From solidworks to URDF?
See http://wiki.ros.org/sw_urdf_exporter

## Slide 16: 3. spawn the robot in the world
By running node spawn_model of gazebo_ros package

## Slide 17: 4. publish joints states

## Slide 18: 5. publish robot states

## Slide 19: 6. run rviz

## Slide 20: How does sensor work in Gazebo
How do these three sensors work in Gazebo?
1. Laser
2. odometry
3. Camera

## Slide 21: Laser
Using Gazebo plugins with ROS:
http://gazebosim.org/tutorials?tut=ros_gzplugins

## Slide 22: Odometry
Link for the code: http://docs.ros.org/jade/api/gazebo_plugins/html/gazebo__ros__diff__drive_8cpp_source.html
http://docs.ros.org/indigo/api/gazebo_plugins/html/gazebo__ros__diff__drive_8h_source.html

## Slide 23: 3. Camera
Link for the code:
http://docs.ros.org/diamondback/api/gazebo_plugins/html/gazebo__ros__camera_8h_source.html
http://docs.ros.org/indigo/api/gazebo_plugins/html/gazebo__ros__camera_8cpp_source.html

## Slide 24: Example: Robotic fish
Video: